## Announcement: Differential pressure transmitter P34

Configurable transmitter for pressure and volume flow for installation in a control cabinet

- For measuring positive or negative pressures, even asymmetrically

- Also for volume / mass flow and flow rate measurements

- With temperature input (optional) and built-in, static pressure sensor for P/T compensated volume flow

- With USB port

- Compact housing for control cabinet with IP 20 for top hat rail mounting, without display

- Measurement ranges from 0..10 Pa to 100 kPa

- Measurement ranges / outputs can be configured

- With 2 relay outputs (optional)

- Inductive measurement cell for highly accurate measurement and temperature stability

- High zero point stability thanks to automatic zero point calibration

- Built-in valve provides a high level of overload protection

- Can be calibrated (ex works and on-site)

- CE, GOST and CSA approved

Technical data

Measurement

ranges: 	10/50/100/250/500 Pa, 1/2.5/5/10/20/50/100 kPa (others available upon request, adjustable measurement ranges for volume flow, mass flow and flow rate)
freely scalable from 10..100 % within a measurement range

Analog outputs: 	0..10 V, 0..20 mA, 
4..20 mA

Power supply:	24 VAC/DC

Contact points: 	2 switching relays
max. 230 VAC, 6 A

Margin of error: 	0.2 % of the scaled range, min. 0.3 Pa (optional) 
0.5% of the scaled range (standard)

Temperature
coefficient margin: 0.03 % of max. value/K

Temperature
coefficient

zero point:	± 0 % (cyclical zero-point correction)

Max. system pressure/

overload capacity: 	600 kPa for measurement ranges ≥ 2.5 kPa

200x for measurement ranges < 2.5 kPa

Medium:        	Air, all non-aggressive gases

Sensor 
response time: 	25 ms

Time constant:	20 ms.. 60 s (adjustable)

Operating

temperature:	10°C .. 50°C,

Storage

temperature: 	-10°C .. 70°C

Power
consumption:	approx. 6 VA

Weight: 	approx. 0.45 kg

Pressure ports: 	for hose 4 .. 6 mm

Housing: 	control cabinet ABS housing for top hat rail mounting

Protection class:	IP 20

Dimensions:	125 mm x 108 mm 
x 35.2 mm

Certificates:	CE, CSA, GOST

Data interface:	USB (data cable supplied)

Certificates (opt.):  DAkkS calibration certificate,

ISO factory calibration certificate

Designation:	Differential pressure transmitter

Type: 	P34

Manufacturer: 	halstrup-walcher GmbH